## Slide 1: HIBI v2 to v3
Last modification:
Lasse Lehtonen, 2010-11-30

## Slide 2: About
This document briefly explains changes made from hibi_v2 to hibi_v3
Assumes that readers are familiar with hibi_v2

## Slide 3: General stuff
Some file names have been changed to match entities and files containing multiple entities splitted
Only tested files have been copied to v3 directory
  Missing files include wrapper r2 and most bridges
  Don’t copy them over until they have been verified to work for both the multiplexed and separated address bus versions

## Slide 4: Deprecated stuff
Broadcast / multicast commands for data and messages
  multicast_en_g removed
  id zero is still segment wide broadcast id for configure commands
Old command constants
Base_id_g generic (wasn’t used anyway)
  there’s empty place in cfg_mem now

## Slide 5: New stuff
Optionally address is sent with every word
  separate_addr_g generic (details later in this doc)
Bridges will forward config mem reads/writes
  id_min_g and id_max_g generics define the id range to forward (invert_addr_g inverts that)
  id_min_g and id_max_g must be set to zero for others than bridges!
Address range can be freely set
  addr_g to addr_limit_g, if addr_limit_g is zero then the old mask style is used to calculate the upper limit
  This means that you can’t have agent with only address zero
New commands and command constants
  details later

## Slide 6: if separate_addr_g == 1
Address is sent with every word
For wrappers r1 and r4 data_width_g must be the actual data width + addr_width_g!
For wrapper r3 they are as one would expect
  data_width_g for data ports and addr_width_g for address ports
Address
Data
data_width_g
addr_width_g
LSB
MSB
data_in/out:

## Slide 7: Commands 1/2
DATA = low priority, MSG = high priority
WR, RD, WRNP, RDL, WRC intented to be used as defined in OCP-IP docs
DATA_WR_c, MSG_WR_c
  posted write, non-posted write (same as the old write command)
DATA_RD_c, MSG_RD_c
  Normal read
DATA_WRNP_c, MSG_WRNP_c
  , receiving agent should notify the sender (doesn’t affect hibi)
DATA_RDL_c, MSG_RDL_c
  Linked read, target agent should flag the read whatsoever, any writes to flagged whatsoever removes the flag
DATA_WRC_c, MSG_WRC_c
  Conditional write, if target agent’s whatsoever is still flagged the write succeeds. If it’s not flagged then the write should not take place and the receiving agent should send an error packet back to the sender (this doesn’t affect hibi)
CFG_WR_c
  configure memory write, id 0 is segment wide broadcast
CFG_RD_c
  configure memory read , id 0 is segment wide broadcast
  data sent is the return address

## Slide 8: Commands 2/2
EXCL_LOCK_c
  will lock every receiver on its path including bridges. Also the send side fifo multiplexers will be locked (and read side for wrapper_r4)
  Locked receivers will accept only EXCL_WR_c, EXCL_RD_c or EXCL_RELEASE_c commands until lock is released
  Agent shall not send any other commands than EXCL_WR_c and EXCL_RD_c between EXCL_LOCK_c and EXCL_RELEASE_c! (high deadlock risk)
  This command is forwarded to the final target agent
  One data word payload only!
EXCL_RELEASE_c
  Will release all locks on its path
  Is forwarded to the final target agent
  One data word payload only!
EXCL_WR_c
  Exclusive write, passes also non locked receivers
EXCL_RD_c
  Exclusive read, for uninterrupted read-modify-write operations
  Passes also non locked receivers
  EXTREMELY HAZARDOUS DEADLOCK MAKER!