## Slide 1: UDP2HIBI
Jussi Nieminen
Last update 11.1.2010

## Slide 2: Purpose
Connect FPGA board to PC
  Use cross-connected ethernet cable
Structure
  Controller for Ethernet chip
  Block for handling UDP headers
  Adapter to interface with HIBI

## Slide 3: Use case example
Transferring data between a PC and an SDRAM
Nios controls the events but the transfer itself happens between the SDRAM and the PC
In the name of simplicity, some less relevant blocks have been left out from the following diagrams
HIBI
NIOS2HIBI
NIOS II
UDP2HIBI
UDP/IP
Ethernet
controller
HIBI SDRAM
controller
SDRAM

## Slide 4: Data from PC to SDRAM

## Slide 5: Data from SDRAM to PC

## Slide 6: HIBI UDP Basics
Interface between a UDP/IP block and the HIBI bus
Capable of handling one transmission and one incoming packet at a time
UDP2HIBI uses HIBI addresses to separate transfers from different agents
  So all agents must use different addresses when sending to UDP2HIBI

## Slide 7: Tx side
Before a transfer can begin, the UDP2HIBI must be configured by sending a configuration packet
  Sets destination IP address and UDP ports
  Locks the UDP2HIBI to the used hibi address so that no one else can interfere with the transfer.
The transfer is started with a specific tx header
  Sets the tx length
  After the header all words sent by that agent are considered as data until tx length of bytes has been received
After the transmission the UDP2HIBI must be released with a release packet so that others can use it

## Slide 8: Sequence diagram
CPU 2
CPU 1
UDP2HIBI
Tx configuration
To addr: 0x01234567
Ack
UDP2HIBI locked to address 0x01234567
Tx configuration
Nack
To addr: 0x01234568
Tx data
To addr: 0x01234567
Tx data
To addr: 0x01234567
Tx data
To addr: 0x01234567
Tx data
To addr: 0x01234567
Tx data
To addr: 0x01234567
Tx configuration
Nack
To addr: 0x01234568
Tx release
To addr: 0x01234567
UDP2HIBI no longer locked to address 0x01234567
Tx configuration
Ack
To addr: 0x01234568
UDP2HIBI locked to address 0x01234568
Tx data
To addr: 0x01234568
Last data received
UDP2HIBI refuses other communication attempts while locked
The first data transfer must contain a Tx header with tx length
And so on...

## Slide 9: Rx side
Agents can connect UDP/IP addresses (IP address, UDP ports) with their own hibi addresses by sending UDP2HIBI an rx configuration packet
  The information is stored to a receiver table so different agents can connect different IPs/ports to their own addresses
  Wildcard values (all ones, e.g. Port 0xFFFF) can also be used
An ack packet is sent if there was room in the table, nack otherwise
  Future work includes adding a possibility to remove a table entry
If the IP address/ports of a received transmission match with a table entry, the packet gets forwarded to the corresponding hibi address
  Otherwise the transmission is simply discarded

## Slide 10: Used packet types
Following slides introduce the packets and headers used with UDP2HIBI
The ones from 1 to 4 are sent by agents to UDP2HIBI, and 5 to 7 vice versa

## Slide 11: Used packet types (1/7)
Tx configuration
  Feeds UDP2HIBI with Tx parameters
    Destination IP address
    Destination UDP port
    Source UDP port
    Timeout value
  Sender’s HIBI address is there to enable sending of an ack/nack
  Locks UDP2HIBI to the HIBI address that this packet is sent to (not to the sender’s address)
    Packets sent to other UDP2HIBI’s HIBI addresses will be replied with a nack
4 bits:
0x0
28 bits:
Timeout value
32 bits:
Destination IP address
16 bits:
Dest. UDP port
16 bits:
Source UDP port
31...28,27...........................................................0
31.......................................................................0
31..............................16,15................................0
32 bits:
Sender’s HIBI address
31.......................................................................0

## Slide 12: Used packet types (2/7)
Tx data
  0x1 indicates start of a Tx
  Tx length is given in it’s own field
  After the Tx data header all received words from the same sender (sent to the same HIBI address) are treated as data
    Tx is considered complete when tx length of words has been received or timeout stops the activity
4 bits:
0x1
11 bits:
Tx length (n)
8 bits:
Data 0
17 bits:
Don’t care
31....28,27..............17,16....................................0
31...........24,23...........16,15............8,7...............0
8 bits:
Data 1
8 bits:
Data 2
8 bits:
Data 3
...
8 bits:
Data n-2
31...........24,23...........16,15............8,7...............0
8 bits:
Data n-1
8 bits:
Don’t care
8 bits:
Don’t care

## Slide 13: Used packet types (3/7)
Tx release
  Releases UDP2HIBI’s address lock to make the block usable for others again
4 bits:
0x2
28 bits:
Don’t care
31...28,27...........................................................0

## Slide 14: Used packet types (4/7)
Rx configuration
  Connects a HIBI address with a certain source IP address and UDP source/destination ports
  Any incoming transfer that matches the address and ports will be sent to given HIBI address
  An ack/nack will be sent to the given HIBI address to announce success of the operation
4 bits:
0x3
28 bits:
Don’t care
32 bits:
Source IP address
16 bits:
Dest. UDP port
16 bits:
Source UDP port
31...28,27...........................................................0
31.......................................................................0
31.............................16,15.................................0
32 bits:
Destination HIBI address
31.......................................................................0

## Slide 15: Used packet types (5/7)
Rx data
  Header type 0x4 indicates start of an icoming transmission
  Rx length in it’s own field
  After the header, data words follow until all has been sent (Rx length of bytes)
4 bits:
0x4
11 bits:
Rx length (n)
8 bits:
Data 0
17 bits:
Don’t care
31....28,27...............17,16...................................0
31...........24,23...........16,15............8,7...............0
8 bits:
Data 1
8 bits:
Data 2
8 bits:
Data 3
...
8 bits:
Data n-2
31...........24,23...........16,15............8,7...............0
8 bits:
Data n-1
8 bits:
Don’t care
8 bits:
Don’t care

## Slide 16: Used packet types (6/7)
Ack
  Acknowledges a received configuration packet
  After Tx configuration packet:
    bit 27 = ’1’
    Means that the UDP2HIBI has been locked to the used HIBI address and is ready to transfer
  After Rx configuration packet:
    bit 27 = ’0’
    Given parameters have successfully been saved to the rx address table
4 bits:
0xF
28 bits:
Don’t care
31....28, 27 ,26................................................0
1 bit:
Tx/Rx

## Slide 17: Used packet types (7/7)
Nack
  Configuration packet not received
  After Tx configuration packet:
    bit 27 = ’1’
    Means that the UDP2HIBI has been locked to some other HIBI address and is not available right now
  After Rx configuration packet:
    bit 27 = ’0’
    No room for new entries in the Rx address table
4 bits:
0xF
28 bits:
Don’t care
31....28, 27 ,26................................................0
1 bit:
Tx/Rx

## Slide 18: Future work
Possibility to delete a receiver table entry
Possibility to reset the block via HIBI
Maybe a table for transfer information too
  Only one configuration packet needed per agent
  Tx data header would result in an ack/nack according to UDP2HIBI state
  No release packets
    UDP2HIBI would release the lock automatically after transferring tx length of data
  Testing and user experiences needed to see if this is worth doing

## Slide 19: UDP2HIBI implementation
Jussi Nieminen
Last update 18.1.2010

## Slide 20: Contents
Overview
Block diagram
Introduction of the separate blocks
Table of used generics with explanations

## Slide 21: Overview
Block that connects HIBI with UDP/IP
2170 lines of VHDL (18.1.2010)
Divided into five subblocks

## Slide 22: Block diagram
Ctrl
regs
HIBI
receiver
HIBI
transmitter
HIBI wrapper
UDP/IP
Tx ctrl
Rx ctrl
UDP2HIBI

## Slide 23: HIBI receiver
Reads data from HIBI and decides what to do with it
  Recognises different headers and acts accordingly
    see UDP2HIBI.ppt for information about the headers
Writes data directly to the multiclk fifo of the TX ctrl block
Feeds TX ctrl and ctrl regs with needed tx information

## Slide 24: Tx ctrl
Manages outgoing transfers
  Communicates with the UDP/IP block
    UDP/IP reads data directly from the multiclk fifo
  Tx information (address, ports) comes from the ctrl regs
Handles timeouts
  When timeout occures, informs the ctrl regs and starts writing zeroes to the multiclk fifo to complete the current transfer

## Slide 25: Ctrl regs
Control registers, kind of a status register bank of the system
Contains
  Tx information
    Destinaton address, udp ports
  Lock information
    Lock state (locked or not)
    HIBI address that the block is locked to
  Receiver table
    Connects rx info (source addr, ports) to receiving HIBI address
Commands HIBI transmitter to send (n)acks when necessary

## Slide 26: Rx ctrl
Communicates with the UDP/IP block rx side
Has two fifos, a 16-bit-wide multiclk fifo and a 32-bit-wide normal fifo
  Handles the data width conversion between the fifos
  32-bit fifo makes it easier for the HIBI transmitter to send data
Gets the receiving HIBI address from the receiver table of the ctrl regs block
  If the rx information (source address, UDP ports) don’t match any table entries, the data is discarded

## Slide 27: HIBI transmitter
Sends stuff to HIBI wrapper
  Acks/nacks or data from transfers
The rx ctrl commands sending of transfers and the ctrl regs commands sending of (n)acks
  Awaiting (n)ack requests are stored to an ack fifo
    Acks have higher priority over the regular transfers
  If there are too many (n)ack requests in a small period of time, the ack fifo may become full and discard further requests
    Make sure that the size of the ack fifo is adequate (with generic ack_fifo_depth_g)
    More agents using the UDP2HIBI means more possible parallel ack requests

## Slide 28: Generics
Generic name | Default value | Explanation
receiver_table_size_g | 4 | Amount of possible receiver table entries
ack_fifo_depth_g | 4 | Size of the ack request fifo
tx_multiclk_fifo_depth_g | 10 | Síze of the tx multiclk fifo
rx_multiclk_fifo_depth_g | 10 | Size of the rx multiclk fifo
hibi_tx_fifo_depth_g | 10 | Size of the fifo between rx multiclk and HIBI transmitter
hibi_data_width_g | 32* | Width of the HIBI bus
hibi_addr_width_g | 32 | Width of a HIBI address
hibi_comm_width_g | 3* | Width of a HIBI command
frequency_g | 50000000 | System frequency, must be a multiplicand of 25MHz (UDP block frequency) for the multiclk fifos to work
Values marked with * cannot be altered without some (possibly huge) modifications to the source code.

## Slide 29: Controller for DE2 board’s Ethernet chip, including UDP functionality
Jussi Nieminen, Erno Salminen
TUT
October 2009

## Slide 30: Contents
Purpose
Block diagram
Basic functionality
Interface
Usage
Current restrictions

## Slide 31: Purpose
Made for communication between a DE2 board and a single PC
  Not sophisticated enough to be connected to a network
  The PC and FPGA applications must know what can and what cannot be sent
  More details in the Restrictions slide
Originally designed for a Network-on-Chip monitor application requiring high bandwidth from FPGA to PC

## Slide 32: Block diagram
Two blocks
  Ethernet chip interface
  UDP/IP interface
The blocks in the diagram are not in scale
The current version (UDP/IP and DM9kA controller) takes a little under 2000 logic cells (from the 33,216 of the DE2’s)
UDP/IP headers
ARP
DM9kA
controller
DM9000A
Application
FPGA
UDP/IP
Eth chip

## Slide 33: Basic functionality
UDP/IP and DM9kA controller are two separate blocks, so UDP/IP part can also be used with other ethernet controller chips
ARP (address resolution protocol) block handles both ARP requests and replies, so applications (both in PC or in FPGA) don’t have to worry about MAC addresses
After the MAC addresses have been resolved, the UDP/IP block simply inserts or removes headers from outgoing and incoming packets
UDP/IP headers
ARP
DM9kA
controller
DM9000A
Application
FPGA
UDP/IP

## Slide 34: Interface
Application
(e.g. UDP2HIBI block)
UDP/IP
new_tx
tx_length (11b)
destination_address (32b)
destination_port (16b)
source_port (16b)
tx_data (16b)
tx_data_valid
tx_read_enable
rx_read_enable
new_rx
source_address (32b)
source_port (16b)
destination_port (16b)
rx_length (11b)
rx_erroneous
rx_data (16b)
rx_data_valid

## Slide 35: Usage
When sending a packet, the application must give UDP/IP block following information
  Destination IP address
  Source port
  Destination port
  Transfer length
The application must also place valid data to data bus and raise a data_valid signal
  When the UDP/IP block is ready, it reads data by raising its read_enable signal
  Data bus is 16 bits wide consisting of two separate bytes

## Slide 36: Usage (2)
When the UDP/IP block has received a packet, it feeds the application with following information
  Source IP address
  Source port
  Destination port
  Transfer length
  Indication if transfer is somehow erroneous
The data itself is moved in a similar manner as when transmitting
  UDP/IP writes data to the data bus and raises data_valid signal
  The application reads the data by raising read_enable signal

## Slide 37: Current restrictions
Most of the IP header fields are unusable
  In addition to addresses and length fields, only checksum computation is done
    No flags, options etc.
  No support for packet fragmenting
    Length of a transfer < max ethernet frame size (1518 bytes)
Only UDP packets supported, packets of other protocols are simply discarded