## Slide 1: HIBI v3
Pictures for documentation

## Slide 2: General layout
HIBI segment
PCIe to HIBI
Cmp 0
HIBI phy
Hibi wrapper R3
Hibi wrapper R3

## Slide 3: General layout
HIBI wrapper R3
HIBI wrapper R1
addr_data_mux_write
addr_data_mux_write
addr_data_mux_read
addr_data_mux_read
message interface
normal interface
HIBI segment
HIBI component

## Slide 4: HIBI wrapper resource usage – Arria II GX
HIBI wrapper R3
HIBI wrapper R1
addr_data_mux_write
addr_data_mux_write
addr_data_mux_read
addr_data_mux_read
message interface
normal interface
HIBI segment
HIBI component
HIBI wrapper fifo:
width: 38 bits (data 32, address_valid 1, comm 5)
size: 4 words
comb. aluts: 76-104
registers: 155-167
4 fifos in 1 R1 wrapper
HIBI wrapper R3:
comb. aluts: 724-763
registers: 1039-1168
HIBI wrapper R1:
comb. aluts: 466-533
registers: 825-935
comb. aluts: 533
registers: 935
comb. aluts: 533
registers: 935
comb. aluts: 533
registers: 935
comb. aluts: 533
registers: 935

## Slide 5
HIBI wrapper R1
double fifo demux write
transmitter
receiver
HIBI segment
HIBI component
double fifo demux read

## Slide 6: General layout
HIBI wrapper R3
HIBI wrapper R1
addr_data_mux_write
addr_data_mux_write
addr_data_mux_read
addr_data_mux_read
message interface
normal interface
HIBI segment
HIBI component
HIBI wrapper R1
double fifo demux write
transmitter
receiver
double fifo demux read
double fifo demux write
fifo
fifo
double fifo demux read
fifo
fifo
fifo mux read

## Slide 7: HIBI v3 resource usage
  Onchip memories can also be used for the HIBI wrapper fifos
  Requires atleast 12 m9k blocks per wrapper on a Arria II GX (one m9k memory 18 bits wide in two port mode, 32-bit HIBI wrapper fifo 38 bits wide)

## Slide 8: HIBI v3 performance
troughput of a 32-bit HIBI segment, data and address on the same bus, transfer between two HIBI components without other signal traffic, 1024 word transfer:
  Theoretical max performance would be achieved in 1025 cycles (1024 data cycles + 1 address cycle)
  Wrapper fifo size 4 words: 1847 cycles
  Wrapper fifo size 5 words: 1600 cycles
  Wrapper fifo size 6 words: 1185 cycles
  Wrapper fifo size 7 words: 1168 cycles
  Wrapper fifo size 8 words: 1181 cycles
  Wrapper fifo size 9 words: 1180 cycles
  Wrapper fifo size 10 words: 1167 cycles
  Wrapper fifo size 11 words: 1175 cycles
  Wrapper fifo size 64 words: 1114 cycles
  Wrapper fifo size 256 words: 1077 cycles

## Slide 9: HIBI v3 performance
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 64 | 256
HIBI transfer time | 1847 | 1600 | 1185 | 1168 | 1181 | 1180 | 1167 | 1175 | 1114 | 1077
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 64 | 256
HIBI throughput | 443530048.7277 | 512000000 | 691308016.8776 | 701369863.0137 | 693649449.619 | 694237288.1356 | 701970865.467 | 697191489.3617 | 735368043.088 | 760631383.4726